LESSON 91

EXTRANET

In the late 1990’s and early 2000,

several industries started to use the

term “extranet”.

It describes central repositories of

shared data made accessible via the

web only to authorised members of

particular work groups.

Currently extranet’s usages has

expanded to even allowing customers

and affiliates to access the web site of

a company.

WHAT IS EXTRANET

An extranet is a private network that

uses Internet technology and public

telecommunications system to

securely share relevant information

with authorised parties.

Only registered or authorised users

can navigate or access the extranet.

USES OF EXTRANET

Extranet can be used to:

Share product catalogues with

wholesalers.

Jointly develop programs with

other companies.

Provide access services given by

one company to a group of

other companies.

Share news of common interest

exclusively with partner

companies.

198

M. Amin, SMK Raja Shahriman

INTERNET AND EXTRANET

LESSON 92

M. Amin, SMK Raja Shahriman

COMMUNICATION DEVICES : HARDWARE REQUIREMENTS

Communication devices are hardware

components that enable a computer to send

or receive data, instructions and

information to and from one or more

computers.

Examples of communication devices are:

Network Interface Card (NIC)

Wireless Network Interface Card

(WNIC)

internal and external modem

hub or switch

router

wireless access point

NETWORK INTERFACE CARD

A network card, sometimes pronounced as NICK, is an adapter card or PC

card  that enables the computer to access the network.

199

WIRELESS NETWORK

INTERFACE CARD

Wireless Network Interface Card is a network card

that provides wireless  data transmission.

M. Amin, SMK Raja Shahriman

NETWORK COMMUNICATION CHANNELS

There are two types of modem, internal modem and external modem. An

internal modem only works in stand-alone computers. It is built into the

computer.

An external modem is separated from the computer and is also mobile.

HUB/SWITCH

Hub or switch is a common connection point for devices in a network. Hubs

are commonly used to connect segments of a LAN.

200

ROUTER

M. Amin, SMK Raja Shahriman

A router is a communications device that connects multiple computers or

other routers together and transmits data to the correct destination.

WIRELESS ACCESS POINT

A wireless access point is a central communications device that allow

computers to transfer data. This device can help information to be

transferred wirelessly to other wireless devices or to a wired network.

Wireless access point has high quality antennas for optimal signals.

201

LESSON 93

M. Amin, SMK Raja Shahriman

FUNCTIONS OF COMMUNICATION DEVICES

NETWORK INTERFACE CARD

A Network Interface Card is a piece of computer hardware designed to allow

computers to communicate over a computer network. The card implements

the electronic circuitry required to communicate using a specific physical

layer and data link layer standard such as ethernet or token ring.

202

M. Amin, SMK Raja Shahriman

WIRELESS NETWORK INTERFACE CARD

A Wireless Network Interface Card or WNIC is a

network card which connects to a radio-based

computer network.

WNIC is an essential

component for wireless

desktop computer. This card

uses an antenna to

communicate through

microwaves.

WNICs are designed around the IEEE 802.11 standard

which sets out low-level specifications on how all

wireless networks operate and can operate in two

modes known as infrastructure mode and ad hoc mode.

INFRASTRUCTURE MODE

In an infrastructure mode network the WNIC

needs an access point: all data is transferred

using the access point as the central hub. All

wireless nodes in an infrastructure mode

network connect to an access point. All nodes

connecting to the access point must have the

same service set identifier as the access point.

AD HOC MODE

In an ad hoc mode network the WNIC does not

require an access point, but can directly

interface with all other wireless nodes directly.

All the peer nodes in an ad hoc network must

have the same channel and service set

identifier.

203

MODEM

A modem is a device that enables a

computer to transmit data over

telephone or cable lines.

Computer information is stored digitally,

whereas information transmitted over

telephone lines is transmitted in the form

of analog waves. A modem converts

between these two forms.

HUB / SWITCH

M. Amin, SMK Raja Shahriman

Hubs are commonly used to connect segments of a LAN. A hub contains

multiple ports.

When a packet arrives at one port, it is copied to

the other ports so that all segments of the LAN can

see all the packets.

A hub connects all the devices on its ports

together. A switch understands when two

devices want to talk to each other, and

gives them a switched connection.

ROUTER

A router is a computer

networking device that

forwards data packets

across a network toward

their destinations,

through a process

known as routing.

A router acts as a junction between two or more networks to transfer data

packets among them. In order to route packets, a router communicates with

other routers using routing protocols.

204

WIRELESS ACCESS POINT

M. Amin, SMK Raja Shahriman

A wireless access point is a device that connects wireless communication

devices together to form a wireless network.

Wireless access point (or Wireless AP) usually connects to a wired network

and can relay data between wireless devices and wired devices.

Several Wireless APs can link together to form a larger network that allows

"roaming". Wireless access points have IP addresses for configuration.

LESSON 94

TRANSMISSION MEDIUM

In communications, transmission is the sending of electrical messages in the

form of wave or energy. Transmission medium means any material

substance which can propagate waves or energy.

Computers and other telecommunication devices use signals in a form of

wave or energy to represent data which are sent through a transmission

media.

205

TYPES OF TRANSMISSION MEDIA

M. Amin, SMK Raja Shahriman

Transmission media can be divided into two broad categories. The physical

transmission media, or guided medium and the wireless transmission media.

The twisted-pair cable, coaxial cable and fibre

optic cable are examples of physical transmission

media.

Wireless transmission medium or unguided

medium is through air.

PHYSICAL TRANSMISSION MEDIUM

In physical transmission medium,

waves are guided along a solid

transmission medium.

Wireless transmission medium

waves are unguided and the

transmission and reception are by

means of antennas.

In our daily activities we probably use both media consciously or

unconsciously.

For example, we use physical transmission medium when we:

connect a PC to a printer   using parallel port or USB  port

connect a PC to the same   phone line for Internet  communication

such as   TMNET Streamyx.

PCs are connected using  twisted-pair cables to wall  sockets in the

office

206

We use wireless transmission medium when we:

listen to the radio

talk over the telephone

M. Amin, SMK Raja Shahriman

use hotspots that have wireless Internet access with WiFi technology

at restaurants and airports.

WIRELESS TRANSMISSION MEDIA

Wireless data transmission means data communication between network

devices without using cables or cords, but by using radio frequency or

infrared waves.Wireless data transmission is categorised into short, medium

and long range data transmission.

An example for short range is Bluetooth or Infrared. Medium range data

transmission is WiFi or wireless LAN and for long range it is 3G.

3G is a so-called "third-generation” broadband packet-based transmission of

text, digitised voice, video, and multimedia at data rates up to and possibly

higher than 2 megabits per second (Mbps), offering a consistent set of

services to mobile computer and phone users no matter where they are

located in the world. 3G works over wireless air interfaces.

207

TRANSMISSION ENVIRONMENT

M. Amin, SMK Raja Shahriman

In our daily activities, such as talking over the phone, sending short

messages, sending email or uploading files to remote users, will likely

involve a combination of transmission mediums along the way.

The sender and the receiver will also involve many communication devices

especially switches and routers. These devices are interconnected by

transmission mediums that can be from any of the physical or wireless

transmission mediums stated earlier.

In network communications, it is common to represent the interconnection

between devices as network clouds.

LESSON 95

PHYSICAL TRANSMISSION MEDIA

Physical transmission media refers to material substances that can

propagate waves or energy. It is used to guide electrical messages from

one end to the other.

Ethernet and token ring LANs

often use physical

transmission media.

208

M. Amin, SMK Raja Shahriman

CABLES AS A PHYSICAL TRANSMISSION MEDIUM

Cables are used as a physical transmission medium. There are three types of

cables used in transmitting electrical messages. They are:

Twisted-Pair Cable - Two insulated copper

wires that  are twisted around each other.

Each connection on twisted-pair requires

both wires.

Coaxial Cable - A cable consisting of a

conducting outer metal tube that encloses

and is insulated from a central conducting

core, used primarily for the transmission of

high-frequency signals.

Fibre Optic Cable - Glass fibre used for

laser transmission of video, audio and/or

data.

TWISTED-PAIR CABLE

The twisted-pair cable is generally a common

form of transmission medium. It consists of

two wires or conductors twisted together, each

with its own plastic insulation. The twisted

wires cancel out electromagnetic interference

that can cause crosstalk , the noise generated

by adjacent pairs.

The most common connector used for twisted-pair cable is RJ-45.

Electromagnetic

A wave produced by the interaction of time-varying electric and

magnetic fields.

Crosstalk

Undesired coupling of a signal from one circuit, part of a circuit, or channel,

to another.

RJ-45

Registered Jack-45 (RJ-45) is an eight-wire connector used commonly to

connect computers onto Local Area Networks (LAN), especially Ethernets.

209

TYPES OF TWISTED PAIR CABLE

M. Amin, SMK Raja Shahriman

UTP Cable

The Unshielded Twisted-Pair or UTP is the most

common twisted-pair cable used in communications.

It has four pairs of colour-coded twisted-pair cables

that are covered with a plastic outer jacket.

Cables that consist of pairs of unshielded wire twisted together. It is the

most common kind of copper telephone wiring.

The Shielded Twisted-Pair or STP is another form of

twisted-pair cable.

Its four pairs of colour-coded wires are each

wrapped in metallic foil, and all four are then

collectively wrapped in a layer of metallic braid or

foil. Finally, this layer is wrapped with a plastic outer

jacket.

STP Cable

Twisted-pair cable wires that consist of an outer covering or shield.

COAXIAL CABLE

The coaxial cable, often referred to as ‘coax’, consists

of a single copper wire surrounded by at least three

layers.They are an insulating material, a woven or

braided metal and a plastic outer coating.

This cable is often used as cable television

(CATV) network wiring because it can be

cabled over longer distances in comparison

to the twisted-pair cable.

210

PART OF COAXIAL CABLE

M. Amin, SMK Raja Shahriman

The coaxial cable consists of a centre

inner conductor of solid or stranded

wire enclosed in an insulating sheath.

The sheath is enclosed in an outer

conductor of metal foil or a woven

copper braid.

This outer conductor is also enclosed in another insulating sheath, and the

whole cable is protected by a plastic cover.  The outer conductor acts as the

second wire in the cable. It also acts as a shield for the inner conductor and

helps reduce outside interference.

CONNECTORS FOR THE COAXIAL CABLE

The connector most commonly used in

connecting a coaxial cable to a device is

the BNC connector. BNC is short for

British Naval Connector or Bayonet-Neill-

Concelman.

There are three popular BNC connectors. They are:

BNC connector:  used to connect devices such as the TV set

BNC T connector: used in Ethernet networks

BNC terminator: connected at the end of a cable to prevent the

reflection of signals

211

FIBRE OPTIC CABLE

The fibre optic cable is a networking medium

that uses light for data transmission.

The intensity of light is increased and

decreased to represent binary one and zero.

Its core consists of dozens or hundreds of

thin strands of glass or plastic which uses

light to transmit signals.

Each strand, called an optical fibre, is as thin

as a human hair.

Transmission

M. Amin, SMK Raja Shahriman

The act of sending electrical messages (and also radiant energy that passes

through media.)

Binary

The binary system is a way of counting using just the two numbers 0 and 1.

Optical Fibre

A flexible optically transparent fibre, usually made of glass or plastic,

through which light can be transmitted by successive internal reflections.

PARTS OF A FIBRE OPTIC CABLE

Inside a fibre optic cable, each optical fibre is clad

with an insulating glass and a protective coating.

Typically, a fibre optic cable has five parts.

The core is the light transmission element. It is

typically made of glass or plastic.

Cladding surrounds the core.It is also made of

glass or plastic but is less dense than the core.

Buffer surrounds cladding. It is usually made of

plastic and helps shields the core and cladding from

being damaged.

A strengthening material surrounds the buffer to prevent the fibre cable

from being stretched when installers pull it.

Outer jacket surrounds the cable to protect the fibre against abrasion,

solvents and other contaminants.

212

CONNECTORS OF A FIBRE OPTIC CABLE

M. Amin, SMK Raja Shahriman

The most commonly used fibre optic connectors are SC, ST, FC and MT-RJ

connectors.

SC

A fibre optic cable connector that uses a push-pull

latching mechanism similar to common audio and

video cables.

ST

A fibre optic cable connector that uses a bayonet

plug and socket.

FC

A fibre optic cable connector that uses a threaded

plug and socket.

MT-RJ

Mechanical Transfer Registered Jack (MT-RJ), a

fibre optics connector popular for small form factor

devices due to its small size.

LESSON 96

WIRELESS TRANSMISSION MEDIA

WIRELESS COMMUNICATION

Wireless is a method of communication that uses electromagnetic waves

rather than wire conductors to transmit data between devices.Wireless

networks are telephone or computer networks that use radio frequencies

and infrared waves as their carrier.

213

M. Amin, SMK Raja Shahriman

The mediums used in wireless communications

are air, vacuum and even water. Air is the most

commonly used medium. Signals are normally

broadcasted through air and are available to

anyone who has a device capable of receiving

them.

WIRELESS TECHNOLOGY

The use of wireless technology as a

method of data transport appears very

similar to a wired technology.

In a wireless media however, signal

transmission is unguided and the device

communicates without using wires

between nodes, usually by relying on

radio frequencies instead.

WIRELESS TRANSMISSION

Wireless transmission can be categorised into three broad groups:

Radio Waves

Microwaves

Infrared

214

RADIO WAVES

M. Amin, SMK Raja Shahriman

There is no clear difference between radio waves and microwaves.

Electromagnetic waves ranging in frequencies between 3 KHz and 1 GHz are

normally called radio waves. Waves ranging in frequencies between 1 and

300 GHz are normally called microwaves.

It is actually the behaviour of the waves rather than the frequencies that

determines the classification of wireless transmission.

RADIO WAVES SIGNALS

Radio waves are normally omnidirectional.

When an antenna transmits radio waves,

they are propagated in all directions. This

means that the sending and receiving

antennas do not have to be aligned.

The omnidirectional characteristics of radio

waves make them useful for multicasting, in

which there is one sender but many

receivers.

Our AM and FM radio stations, cordless phones and televisions are examples

of multicasting.

DISADVANTAGES OF USING RADIO WAVES

Radio waves transmitted by one antenna are susceptible to interference by

another antenna that is sending signals of the same frequency or band.

215

MICROWAVES

M. Amin, SMK Raja Shahriman

Electronic waves with frequencies between 1 GHz to 300 GHz are normally

called microwaves.

Unlike radio waves, microwaves are unidirectional, in which the sending and

receiving antennas need to be aligned. Microwaves propagation is

line-of-sight therefore towers with mounted antennas need to be in direct

sight of each other.

Due to the unidirectional property of microwaves, a pair of antennas can be

placed aligned together without interfering with another pair of antennas

using the same frequency.

Two types of antenna are used for

microwave communications. They are

the parabolic dish antenna and the

horn antenna.

The parabolic dish antenna receives ingoing

transmissions by reflecting the signal to a common

point called the focus.

Outgoing transmissions are broadcasted

through a horn antenna by deflecting

signals outward in a series of narrow

parallel beams.

High-frequency microwaves cannot penetrate walls. This

is why receiving antennas cannot be placed inside

buildings.

216

INFRARED

Infrared is used in devices such as the mouse,

wireless keyboard and printers. Some manufacturers

provide a special port called the IrDA port that

allows a wireless keyboard to communicate with a

PC.

M. Amin, SMK Raja Shahriman

INFRARED SIGNALS

Infrared signals have frequencies between

300 GHz to 400 THz. They are used for

short-range communication.

Infrared signals have high frequencies and cannot penetrate walls. Due to its

short-range communication system, the use of an infrared communication

system in one room will not be affected by the use of another system in the

next room.

This is why using an infrared TV remote control in our home will not

interfere with the  use of our neighbour’s infrared TV remote control.

DISADVANTAGES OF USING INFRARED

Infrared signals cannot be used for long distance communication. In

addition, we cannot use infrared waves outside a building because sun's rays

contain infrared waves that can interfere with communication.

217

LESSON 97

SERVER SOFTWARE

M. Amin, SMK Raja Shahriman

Software such as Windows Server 2003, Windows NT and Red Hat Linux are

some of the examples of server software. All of these software fall under the

Network Operating System.

DEFINITION OF NETWORK OPERATING SYSTEMS

An operating system is the program that first

loads when a computer boots and manages any

other software or hardware on the computer.

A Network Operating System or known as NOS,

has additional functionality that allows it to

connect computers and peripherals to a network.

A Network Operating System is most frequently

used with Local Area Networks and Wide Area

Networks, but could also have application to

larger network systems.

A NOS is not the same as the

networking tools provided by

some existing operating systems,

Windows XP for instance.

NOS is an operating system that

has been specifically written to

keep networks running at optimal

performance.

EXAMPLES OF NETWORK OPERATING SYSTEMS

Some popular Network Operating

Systems include:

Windows NT

Windows 2000 Server

Windows Server 2003

Red Hat Linux

218

M. Amin, SMK Raja Shahriman

Windows NT is a family of operating

systems produced by Microsoft, the first

version of which was released in July 2003.

It was the first 23-bit version of Windows.

Windows XP and Windows Server 2003 are

the latest versions of Windows NT.

Windows 2000 (also referred to as Win2K

or W2K) is graphical and business-oriented

operating system. It is part of the Microsoft

NT line of operating systems and was

released on February 17, 2000.

Windows 2000 comes in four versions which

are Professional, Server, Advanced Server

and Datacenter Server.

Additionally, Microsoft offers Windows 2000

Advanced Server-Limited edition, which was

released in 2001 and runs on 64-bit Intel

Itanium Microprocessor.

Windows Server 2003 is the name of

Microsoft’s line of server operating systems.

It was introduced in April 2003 as the

successor to Windows 2000 Server.

It is considered by Microsoft to be the

cornerstone of their Windows Server System

line of business server products.

219

M. Amin, SMK Raja Shahriman

Red Hat Linux was one of the most popular

Linux distributions, assembled by Red Hat. It

is one of the “middle-aged” Linux

distributions; 1.0 was released in November

3rd, 1994.

Since 2003, Red Hat has discontinued the

Red Hat Linux line in favour of its new Red

Hat Enterprise Linux.

Red Hat Linux 9, the final release, ended on April 30th,

2004, although the Fedora Legacy project continues

to publish updates.

PEER-TO-PEER NETWORK OPERATING SYSTEMS

Peer-to-peer Network Operating Systems allow

users to share resources and files located on their

computers. It is also for users to access shared

resources found on other computers.

However, they do not have a file server or a

centralised management source.

AppleShare and Windows for Workgroups are

examples of programs that can function as peer-to-

peer Network Operating System.

220

M. Amin, SMK Raja Shahriman

CLIENT/SERVER NETWORKING OPERATING

SYSTEM

Client/server Network Operating Systems allow

the network to centralise functions and

applications in one or more dedicated file

servers. The file servers become the heart of

the system, providing access to resources and

providing security.

Individual workstations or clients

have access to the resources

available on the file servers.

The Network Operating System provides the

mechanism to integrate all the components of

the network and allow multiple users to

simultaneously share the same resources

irrespective of physical location.

Novell Netware and Windows 2000 Server are

examples of client or server Network Operating

Systems.

LESSON 98

CLIENT SOFTWARE

221

FUNCTIONS OF WEB BROWSER

M. Amin, SMK Raja Shahriman

A web browser is a software application that

enables a user to display and interact with

HTML documents hosted by web servers or

held in a file system. Text and images on a

web page can contain hyperlinks to other

web pages at the same or to different

websites.

Web browser allow a user to quickly and easily access information provided

on many web pages at many websites by surfing these links.

Web browsers available for personal computer include Microsoft Internet

Explorer, Safari, Netscape and Opera.Web browsers are the most commonly

used type of Hypertext Transfer Protocol (HTTP) user agent.

Although browsers are typically used to access the World Wide Web, they

can also be used to access information provided by web servers in private

networks or content in file systems.

FUNCTIONS OF EMAIL CLIENT

An email client is a computer program that is

used to read and send email.

FUNCTIONS OF FILE TRANSFER PROTOCOL (FTP)

File Transfer Protocol (FTP) is used to

connect two computers over the Internet

so that the user of one computer can

transfer files and perform file commands

on the other computer.

222

LESSON 99

SETTING NETWORK FACILITIES

NETWORK INTERFACE CARD

A computer, or any computing devices, needs a

network interface to connect to a network and

communicate with other devices on the network.

A Network Interface Card or NIC is an expansion

card that allows the transmission of data over a

cable network.

Also known as a network adapter card, it is an

electronic circuit card that is inserted inside the

computer.

M. Amin, SMK Raja Shahriman

Installing NIC into computers enables the user to connect with other

computers and share not only data but also other devices such as the server

and printer.

Once it is installed, you can connect the network cable from the computer to

the switch or hub. Then, with some software configuration, your computer is

ready for communication on the network.

Inserting or installing a Network

Interface card is not difficult. If you

have installed a modem, a sound

card, or a video controller card on

your computer before, you will

probably find it a simple task to

install a Network Interface Card.

CHECKING FOR A NETWORK INTERFACE CARD

Check whether your PC already has a Network

Interface Card by inspecting the  back of the PC for

a network socket.

223

M. Amin, SMK Raja Shahriman

IDENTIFYING THE LOCATION OF THE NETWORK

INTERFACE CARD

If your PC does not have a Network Interface Card,

then you need to insert one. First you have to

disconnect the power from your PC.

You should remember the dangers of static

electricity. Once the main power supply has been

turned off, touch any

metal part on your computer casing before starting

your work.

Second, carefully remove the casing or side panel of

your PC. Select either the ISA (black) or PCI (white)

slot, depending on the Network Interface Card you

are using.

Third, remove the back blank plate from behind the

slot you have selected for the Network Interface

Card.

224

M. Amin, SMK Raja Shahriman

INSERTING THE NETWORK INTERFACE CARD

Insert the Network Interface Card into the slot you

have selected by firmly pressing the card down.

Secure the card in place with the screw from the

blanking plate.

Replace the casing or side panel of your PC.

Finally, boot the PC and install the driver.

225

LESSON 100

M. Amin, SMK Raja Shahriman

INSTALLING NETWORK INTERFACE CARD (NIC)

INSTALLING THE NIC DRIVER FOR WINDOWS 98

AND WINDOWS ME.

Step 1: After inserting the Network Interface Card

into its slot, the “Add New Hardware Wizard” should

now appear. Click “Next” to continue.

Step 2: Select Search for the better driver and click

“Next” to continue.

Step 3: Select “Specify a location” and browse to

the location where your CD-ROM drive is located.

Select “Next” to continue.

Step 4: Windows will locate the correct driver for

your device on the CD supplied by the library.

Windows will also indicate that it is now ready to

install the driver. Select “Next” to continue.

The NIC driver is now properly installed.

Restart the computer to complete the installation.

226

M. Amin, SMK Raja Shahriman

INSTALLING THE NIC DRIVER FOR WINDOWS 2000

Windows will indicate that it has found a new

hardware after the NIC has been inserted into its

slot. The “Found New Hardware Wizard” will then

appear. Click “Next” to continue.

Step 1: Select "Search for a suitable driver for my

device (recommended)” and click “Next” to

continue.

Step 2: Select “CD-ROM Drives” and click “Next” to

continue. Windows will now search for a suitable

driver for your device.

Step 3: Windows will locate the correct driver for

your device and indicate that it is now ready to

install the driver. Click “Next” to continue.

The NIC driver is now properly installed.

Restart the computer to complete the installation.

227

M. Amin, SMK Raja Shahriman

INSTALLING THE NIC DRIVER FOR WINDOWS XP

Windows will indicate that it has found a new

hardware after the NIC has been inserted into its

slot. The “Found New Hardware Wizard” will then

appear. Click “Next” to continue.

Step 1: Select “Search for the best driver for my

device (recommended)” and click “Next” to

continue.

Step 2: Select “CD-ROM Drives” and click “Next” to

continue. Windows will now search for a suitable

driver for your device.

Step 3: Windows will locate the correct driver for

your device and indicate that it is now ready to

install the driver. Click “Next” to continue.

The NIC driver is now properly installed.

Restart the computer to complete the installation.

228

M. Amin, SMK Raja Shahriman

INSTALLING A WIRELESS NETWORK INTERFACE

CARD DRIVER

Step 1: Place your client adapter in the PCI of your

computer.

Windows will indicate that it has found new

hardware.

The "Found New Hardware Wizard" will then appear.

Click "Next" to continue.

Step 2: Select “CD-ROM Drives” and click “Next” to

continue. Windows will now search for a suitable

driver for your device.

The NIC driver is now properly installed.

Restart the computer to complete the installation.

229

LESSON 101

CRIMPING STRAIGHT CABLE

STRAIGHT CABLE

M. Amin, SMK Raja Shahriman

A network cable acts as an

extension enabling a device with a

Network Interface Card to be

attached to a network.

A common form of network media

is the UTP CAT 5 known as

Unshielded Twisted-Pair Category

5 cable.

ITEMS FOR MAKING STRAIGHT CABLE

CAT 5 CABLE

CAT 5 cable has four twisted pairs of wire for a

total of eight individually insulated wires.

Each pair is colour coded with one wire having a

solid colour:

Blue

Orange

Green

Brown

Twisted around a second wire with a white background and a stripe of the

same colour.

RJ-45

The straight cable is terminated with CAT 5 RJ-45 (Jack)

modular plug (RJ means Registered Jack).

RJ-45 plug are similar to those you'll see on the end of

your telephone cable except they have eight contacts on

the end of the plug and they are about twice as big.

Make sure they are rated for CAT 5 wiring.

230

CRIMP TOOL

CABLE STRIPPER

CUTTERS

M. Amin, SMK Raja Shahriman

Crimp tool - to crimp RJ-45 connectors.

Cable stripper – to cut and strip

cables.

Cutters - to cut the cable off at the reel and to fine

tune the cable ends during assembly.

CABLE CRIMPING PROCESS

The total length of wire segments between a PC

and a hub or between two PCs cannot exceed 100

Meters.

Strip one end of the cable with the stripper or a

cutter.

If you are using the stripper, place the cable in

the groove on the blade (left) side of the

stripper and align the end of the cable with the

right side of the stripper.

Spread and arrange the pairs roughly:

White/Green, Blue

White/Blue, Green

White/Brown, Brown

White/Orange, Orange

231

Trim the ends of the wires so they are even with

one another.

It is very important that the unstripped or

untwisted end be slightly less than half-inch long.

If it is longer than half-inch it will be out of its

specifications and will cause crosstalk.

If it is slightly less than half-inch long, it will not be

properly clinched when RJ-45 plug is crimped on.

There should be little or no space between the

wires.

232

M. Amin, SMK Raja Shahriman

Hold the RJ-45 plug with the clip facing down or

away from you.

Push the wire firmly into the plug.

Inspect it carefully.

Looking through the bottom of the plug, the wire

on the far left side will have a white background

The wires should all end evenly at the front of the

plug.

Hold the wire near the RJ-45 plug with the clip

down and firmly push it into the front-left of the

crimper.

Hold the wire in place and squeeze the crimper

handles quite firmly.

Crimp it once.

Finally test the crimping result.

Test the crimp strength.

If it is done properly, an average person will not be

able to pull the plug off the cable with his or her

bare hands.

233

M. Amin, SMK Raja Shahriman

LESSON 102

CRIMPING CROSSOVER CABLE

M. Amin, SMK Raja Shahriman

This cable can be used to

directly connect two computers

to each other without the use of

a hub or switch.

TOOLS FOR CABLE CRIMPING

What you need are some tools such as a cable, connectors, crimper,

stripper and cutter.

Be sure the cable you are using is properly rated for CAT 5.

Crossover cables are terminated with CAT 5 RJ-45.

STRIPPING CATEGORY 5 CABLE

Start by stripping off about two inches (5cm) of the

plastic jacket off the end of the cable.

CATEGORY 5 CABLE

Category 5 cable must only have half of an inch (1.3

cm) at the end.

CUTTING CATEGORY 5 CABLE

Begin to untwist the twisted exposed wires on your

cable, be sure to hold onto the base of the jacket

with your other hand.

Once you have all the wires untwisted begin to

arrange them in the proper order:

White/Green, Green

White/Orange, Blue

White/Blue, Orange

White/Brown, Brown

234

M. Amin, SMK Raja Shahriman

Once you get all the wired arranged in the proper

order, make sure your wire cutters are within reach

then grasp at the point where they enter the jacket.

Grab your cutters now. Line them up along your

prepared wires about half an inch or 1.3 cm above

the jacket.

Be sure at this point that you are both half an inch or 1.3 cm above the

jacket, and that your cutters are aligned straight across the wires.

FITTING RJ-45 PLUG

Take RJ-45 plugs and begin to slide the wires into

the RJ-45 plugs.

You might face some difficulties at this point, but

have some patience and hold onto those wires.

It will fit in there just fine. Once it is in as far as it

will go the wires should extend almost to the front

of the RJ-45 plugs, and about 3/8 of an inch or 2 cm

of the jacket will be inside the RJ-45 plugs.

CRIMPING CATEGORY 5 CABLE

Be sure to keep a good grip on the RJ-45 plug

and the cable.

Insert the RJ-45 plug into the crimper.

It should only go in one way, so you don't

have to worry about inserting it.

Begin to compress those crimpers.

You will hear a clicking sound. Keep

squeezing.

If you try to let go too early, nothing will

happen. They will not release.

Keep compressing until they stop clicking or

stop moving all together.

At this point, you should be able to let go of

the RJ-45 plug and the crimpers.

235

M. Amin, SMK Raja Shahriman

EXAMINING THE CRIMPED CATEGORY 5 CABLE

If you look at the end of the RJ-45 plug, you

should see that the copper connectors should not

be pressed down into the wires.

Toward the back of the RJ-45 plug it should be

crimped securely holding the jacket or cable in the

RJ-45 plug.

LESSON 103

CONFIGURATION OF NETWORK

Step 1

The first step is to open the Control Panel window.

Step 2

Select Network and Internet Connections.

236

Step 3

M. Amin, SMK Raja Shahriman

Click on the Network Connections icon.

Step 4

Inside the Network Connections window, right

click on Local Area Connection icon.

Then click on Properties in the drop down menu.

Step 5 (A)

Make sure the TCP/IP is one of the items in the

list of connection items.

If TCP/IP is available, proceed to Step 6

If TCP/IP is not available, click on the Install

button.

Step 5 (B)

In the next dialog box, Select Protocol and click

Add… button.

237

M. Amin, SMK Raja Shahriman

Once inside the Protocol dialog box, install the

Internet Protocol (TCP/IP)

Then, proceed to step 6.

Step 6

In the next dialogue box, click on Internet Protocol

(TCP/IP) icon.

Then click on the properties button.

Step 7

After the properties button is clicked, the Internet

Protocol (TCP/IP) Properties window will appear.

You will see details like IP address, Subnet mask

and Default gateway.

Subnet mask specifies the size of the network.

Here, we usually use 255.255.255.0 for small

networks.

Gateways are used to connect to other networks

and the Internet.

238

Step 8

M. Amin, SMK Raja Shahriman

LESSON 104

Select Use the following IP address .

Fill in the network information given by your

teacher for the following.

IP address

Subnet Mask

Default Gateway (optional)

Preferred DNS Server (optional)

Click the OK button when done.

Finally, close all windows. You must restart your

computer before the setting take effect.

TESTING OF NETWORK

Once you have installed the network card, cables and software, you can test

the new TCP/IP protocol. Ping is the best utility for a  TCP/IP connection test.

TESTING OF NETWORK

To use ping, open the Command Prompt window.

Enter the name or IP address you want to test

after the ping command.

The ping utility then sends and receives packets

of information.

If you successfully sent and received packets, all

is well with the TCP/IP connection.

239

If ping displays error messages such as:

•   request timed out

•   unknown host

•  could not send, receive packets over the

network

You should verify that the IP is valid.

M. Amin, SMK Raja Shahriman

If the problem still persists, you have to check your network adapter or

protocol.

LESSON 105

SHARED FOLDER

In Windows, Macintosh and other operating systems, a

folder is a named collection of a related files that can be

retrieved as on entity.

Folders can contain many different types of file, such as

documents, music, pictures, videos and programs.

These files can be copied or moved to other folders,

computers and even to the Internet.

You can also create folders within folders.

You can share the files and folders stored on

your computer, and on your network.

240

LESSON 106

WIRELESS AND MOBILE

M. Amin, SMK Raja Shahriman

Wireless and mobile technology allows you to

access the Internet from wherever you are. You no

longer have to be at home or in the office to check

your email or browse the net.

With wireless technology, you can get connected

with anyone from anywhere.

WIRELESS AND MOBILE COMMUNICATION

Wireless is a term used to describe

telecommunications that use electromagnetic

waves rather than some form of wire to carry

signal over part or the entire communication path.

It refers to communication without cables or cords,

but which chiefly uses radio frequency and infrared

waves. This method of communication relies on

low-powered radio waves to transmit data between

devices.

Wireless and mobile communications rely on IrDA

and the wireless networking of computers.

241

Wireless

M. Amin, SMK Raja Shahriman

Wireless is a term used to describe telecommunications that use

electromagnetic waves rather than some form of wire to carry signal over

part or the entire communication path.

Telecommunication

The science of information transport using wire, radio, optical, or

electromagnetic channels to transmit and receive signals for voice or data

communications.

Electromagnetic Waves

A wave produced by the interaction of time-varying electric and magnetic

fields.

Radio Frequency

Frequency of electromagnetic waves used for radio and television

broadcasting.

Infrared Wave

Electromagnetic waves in the frequency range just below visible light

corresponding to radiated heat. IR waves are often used for remote controls.

IrDA

Infrared Data Association (IrDA) is an organisation that defines the infrared

communications protocol. A protocol used by many laptops and mobile

cellular phones to exchange data at short ranges.

WIRELESS TECHNOLOGY

Wireless technology is rapidly evolving, and is playing an increasingly

important role in the lives of people throughout the world. An ever-larger

number of people are relying on this technology both directly and indirectly.

Specialised and exotic examples of wireless communications and control

include:

Global System for Mobile Communication

General Packet Radio Service

Enhanced Data GSM Environment

Universal Mobile Telecommunications System

Wireless Application Protocol

i-Mode

GSM

Global System for Mobile Communications (GSM) is a globally accepted

standard for digital cellular communications system

i-Mode

The Packet-based service for mobile phones offered by Japan's leader in

wireless technology, NTT DoCoMo

242

M. Amin, SMK Raja Shahriman

GLOBAL SYSTEM FOR MOBILE COMMUNICATION

(GSM)

Global System for Mobile Communication (GSM) is

a digital mobile telephone system used in Europe

and other parts of the world. It is the de facto

(widely recognised) wireless telephone standard in

Europe.

de facto

A specification that hasn't been officially established by an accrediting

agency but that is accepted and used as a standard by a majority of

practitioners.

GENERAL PACKET RADIO SERVICE (GPRS)

General Packet Radio Service (GPRS) is a packet-

based wireless communication service that

provides continuous connection to the Internet for

mobile phone and computer users.

GPRS

General Packet Radio Service (GPRS) is a standard for wireless

communications which runs at speeds up to 115 kilobits per second.

Packet

The unit of data that is routed between an origin and a destination on the

Internet or any other packet-switched network.

ENHANCED DATA GSM ENVIRONMENT (EDGE)

Enhanced Data GSM Environment (EDGE) is a

faster version of the Global System for Mobile

(GSM) wireless service.

EDGE

Enhanced Data rates for Global Evolution(EDGE) is a faster version to the

Global System for Mobile (GSM) wireless service designed to deliver data

at rates up to 384 Kbps.

243

M. Amin, SMK Raja Shahriman

UNIVERSAL MOBILE TELECOMMUNICATIONS

SYSTEM (UMTS)

Universal Mobile Telecommunications System

(UMTS) is a broadband, packet-based system.

It offers a consistent set of services to mobile

computer and phone users no matter where they

are located in the world.

UMTS

Universal Mobile Telecommunications System (UMTS) is a third-generation

(3G) broadband, packet-based transmission of text, digitised voice, video

and multimedia at data rates up to 2 megabits per second (Mbps) and offers

global roaming.

Broadband

Transmission over a network in which more than one signal is carried at a

time. Broadband technology can transmit data, audio and video all at once

over long distances.

WIRELESS APPLICATION PROTOCOL (WAP)

Wireless Application Protocol (WAP) is a set of

communication protocols to

standardise the way that wireless devices, such as

cellular telephones and radio transceivers can be

used for Internet access.

Internet

An international network first used to connect education and research

networks, begun by the US government. The Internet now provides

communication and application services to international-based businesses,

consumers, educational institutions, governments, and research

organisations.

Transceiver

A device that performs both transmitting and receiving functions.

WAP

Wireless Application Protocol (WAP) is a specification for a set of

communication protocols to standardise the way wireless devices, such as

cellular telephones and radio transceivers, can be used for Internet access.

244

i-MODE

Smart Phone

M. Amin, SMK Raja Shahriman

i-Mode, the world's first "smart phone service" was

first introduced in Japan.

It not only provides colour and video over

telephone sets but can also be used for Web

browsing.

A cellular telephone that provides digital voice service as well as any

combination of e-mail, text messaging, pager, Web access, voice recognition

as well as picture taking (camera phone).

TYPES OF WIRELESS

Wireless can be divided into four categories. They are:

fixed wireless

mobile wireless

portable wireless

IR wireless

FIXED WIRELESS

Fixed wireless is the operation of wireless devices

or systems in homes and offices. Devices of fixed

wireless are connected to the Internet via

specialised modems.

MOBILE WIRELESS

Mobile wireless is the use of wireless devices or

systems aboard motorised, moving vehicles.

Examples of mobile wireless are the automotive

cell phone.

PORTABLE WIRELESS

Portable wireless is the operation of autonomous,

battery-powered wireless devices or systems

outside the office, home or vehicle. An examples

of portable wireless are cell phones.

245

IR WIRELESS

IR wireless is the use of devices that convey data

via IR (infrared) radiation and is employed in

certain limited-range communications and control

systems.

LESSON 107

MOBILE COMPUTING

Mobile computing is a generic term used

to describe the ability to use technology

to wirelessly connect to and use centrally

located information and/or application

software via small portable and wireless

computing and communication devices.

Nomadic computing is another name for

mobile computing. Here, users can

access the Internet and retrieve data

from anywhere in the world, using

portable computing devices (such as

laptop and handheld computers) in

conjunction with mobile communication technologies.

M. Amin, SMK Raja Shahriman

People using such a system are sometimes referred to as technomads, and

their ability to use that system is referred to as nomadicity.

Nomadic Computing

A computing environment which offers its user access to data or information

from any device and network while he or she is in on the move.

Nomadicity

The tendency of a person, or group of people, to move with relative

frequency.

DEFINING MOBILE COMPUTING

Mobile computing is about the new strategies of

computing that utilise portable or mobile devices

and wireless communication networks.

There are various types of mobile computing

devices. They include the notebook computer,

tablet PC, handheld computer, PDA and

smartphone.

246

Tablet PC

M. Amin, SMK Raja Shahriman

A wireless personal computer (PC) that allows a user to

take notes in his/her natural handwriting using a stylus or

digital pen on a touch screen.

PDA

Handheld computer device used to organise personal

information such as contacts and schedules. Data can

usually be transferred to a desktop computer by cable or

wirelesstransmission.

Smartphone

A cellular telephone that provides digital voice service as

well as any combination of e-mail, text messaging, pager,

Web access, voice recognition as well as picture taking

(camera phone).

Wireless communication technologies commonly used for mobile computing

include the wireless LAN technology, WWAN technology, Bluetooth and IrDA

interfaces.

Mobile computing can be :

Wireless and mobile access to the Internet.

Wireless and mobile access to private intranets.

Wireless and ad hoc mobile access between mobile

computers.

LAN

A group of personal computers and/or other devices, such as printers or

servers, that are located in a relatively limited area, such as an office, and

can communicate and share information with each other.

WWAN

Wireless Wide Area Network (WWAN) is a form of wireless network that uses

cellular network technologies such as GPRS,CDMA2000, GSM, CDPD and

Mobitex to transfer data.

Bluetooth

A wireless networking technology using radio waves that enables users to

send data and voice signals between electronic devices over short distances.

247

M. Amin, SMK Raja Shahriman

TYPES OF MOBILE COMPUTING DEVICES

NOTEBOOK COMPUTER

A notebook computer or notebook is a small mobile

personal computer, usually weighing from one to

three kilograms. Using the technology from

Symbionics Networks Ltd., a wireless LAN adapter

can be made to fit on a PCMCIA card in a laptop or

notebook computer to provide mobile computing.

PCMCIA stands for Personal Computer Memory Card

Industry Association.

PCMCIA

Personal Computer Memory Card International

Association (PMCIA) is an industry group organised

in 1989 to promote standards for a credit card-size

memory or I/O device that would fit into a personal

computer, usually a notebook or a laptop

computer.

TABLET PC

A tablet PC is a notebook or slate-

shaped mobile computer.

Its digitising tablet technology

allows the user to operate the

computer using a stylus or digital

pen and a touch screen instead of

the usual keyboard and mouse.

Most Tablet PCs offer built-in support for wireless networks.

Stylus

A writing device similar to a modern ballpoint pen to write text or draw

lines on a surface as input to a computer or point to menus.

Touch Screen

Display  overlays  which  are  typically  either  pressure-sensitive  (resistive),

electrically-sensitive (capacitive), acoustically-sensitive (SAW - surface

acoustic  wave)  or  photo-sensitive  (infra-red).  The  user  selects,  moves  and

draws by pointing to, and touching, the relevant part of the screen.

248

PDA

Personal digital assistants or PDAs are handheld

devices that were originally designed as personal

organisers but became much more versatile over

the years.

Many PDAs can access the Internet, intranets or

extranets via Wi-Fi or Wireless Wide-Area Networks

or WWANs.

SMART PHONE

A smart phone is an electronic handheld device

that integrates the functionality of a mobile phone

and a personal digital assistant or PDA or

other information appliance.

This is often achieved by adding telephone

functions to an existing PDA  or PDA Phone or

putting “smart” capabilities such as PDA functions

into a mobile phone.

M. Amin, SMK Raja Shahriman

TECHNOLOGIES FOR MOBILE COMPUTING

WIRELESS LAN

A wireless LAN is a technology that allow

notebook users to connect to a Local Area

Network (LAN) through a wireless (radio)

connection.

The IEEE 802.11 group of standards specifies

technologies to be used for wireless LANs.

WWAN

WWAN, which stands for Wireless Wide Area

Network, is a form of wireless network.

Wireless Wide Area Network (WWAN) is a

form of wireless network that uses cellular

network technologies such as GPRS,

CDMA2000, GSM, CDPD and Mobitex to

transfer data.

249

BLUETOOTH

Bluetooth, also known as IEEE 802.15.1, is

a telecommunication industry specification

for wireless Personal Area Networks or

PANs. Bluetooth devices operate on a radio

communication system.

For two Bluetooth devices to communicate,

they do not have to be in line-of-sight. In

fact, they can even be in separate rooms,

as long as the received power is high

enough.

M. Amin, SMK Raja Shahriman

Bluetooth transmits and receives data in a frequency band of 2.45 GHz.

THE INFRARED DATA ASSOCIATION

The Infrared Data Association or IrDA

defines physical specifications of

communication protocol standards for short

range exchange of data over infrared light.

This is used in Personal Area Networks

(PANs).

Among existing uses of IrDA and possible

uses are:

sending a document from a notebook

computer to a printer

exchanging business cards between handheld PCs

coordinating schedules and telephone books between a desktop and

network computers.

PAN

Personal Area Network (PAN) is a computer network used for communication

among computer devices (including telephones and personal digital

assistants) close to one person.

250

M. Amin, SMK Raja Shahriman

COMMON SERVICES FOR MOBILE COMPUTING

To cater to the needs of mobile computing, Wireless

Service Providers would seek to provide wireless access

points for as many wireless network devices as possible

in specified service zones.

Services include:

Services include:

email capabilities

A variety of software applications for secured communications.

Print stations

Tracking and navigation systems

Instant mobile messaging

Mobile secutity services

Mobile data, voive and video systems.

Access to satellitte radio and TV.

Remote home premise video monitor.

LESSON 108

INTERNET TECHNOLOGY

The Internet works wonders to those who are in touch with the technology.

Communication is made easy, economical and fast with the development in

the Internet technology.

Now, we do not have to suffer high telephone bills because of our oversea

calls. The Internet allow us to make voice calls for free, like those services

provided by Skype and Yahoo Messenger.

DEFINITION OF INTERNET TECHNOLOGY

Internet Technology is a broad range of technologies for web development,

web production, design, networking, telecommunication and e-commerce.

251

M. Amin, SMK Raja Shahriman

VOICE OVER INTERNET PROTOCOL (VoIP)

Protocols used to carry voice signals over the IP

network are commonly referred to as Voice over

IP or VoIP. VoIP is one of the Internet

technologies that allows a user to make telephone

calls using a broadband Internet connection

instead of a regular (or analog) phone line.

VoIP is a method for taking analog audio signals

and turning them into digital data that can be

transmitted over the Internet.

VoIP SERVICES

There are three different VoIP services in common use today. They are

Analog Telephone Adapter (ATA), IP Phones and computer-to-computer.

ANALOG TELEPHONE ADAPTER (ATA)

The simplest and most common way is

through the use of a device called an

Analog Telephone Adapter (ATA). The ATA

allows you to connect a standard phone to

your computer or your Internet connection

for use with VoIP.

The ATA is an analog-to-digital converter. It

takes the analog signal from your traditional

phone and converts it into digital data for

transmission over the Internet.

Skype, one VoIP provider, offers free calling locally and between members,

and inexpensive long-distance calls to other numbers.

252

IP PHONES

IP Phones look just like normal phones with

a handset, a cradle and buttons. IP Phones

have an RJ-45 Ethernet connector instead

of the standard RJ-11 phone connectors.

IP Phones connect directly to your router

and have all the necessary hardware and

software onboard to handle the IP Call.

Soon, WiFi IP phones will be available,

allowing subscribing callers to make VoIP

calls from any WiFi hot spot.

COMPUTER-TO-COMPUTER

Computer-to-computer is certainly the

easiest way to use VoIP. Devices needed to

place a computer-to-computer Internet

telephone call:

Software, a microphone, speakers or

headphones, a sound card and an Internet

connection preferably a fast one like you

would get through a cable or DSL modem.

Except for your normal monthly ISP fee,

M. Amin, SMK Raja Shahriman

there is usually no charge for computer-to-computer calls, no matter what

the distance.

ADVANTAGES OF VoIP

As VoIP is digital, it may offer features and

services that are not available with a traditional

phone. If you have a broadband Internet

connection, you need not maintain and pay the

additional cost for a line just to make telephone

calls.

With many VoIP plans you can talk for as long

as you want with any person in the world. You

can also talk with many people at the same time

without any additional cost.

253

DISADVANTAGES OF VoIP

Some VoIP services do not work during

power failures and the service provider

may not offer backup power.

Not all VoIP services connect directly to

emergency services. VoIP providers may

or may not offer directory assistance or

white page listings.

As VoIP uses an Internet connection, it is

susceptible to all the problems normally

associated with home broadband

services.

M. Amin, SMK Raja Shahriman

Phone conversations can become distorted, garbled or lost because of

transmission errors. Some kind of stability in Internet data transfer needs to

be guaranteed before VoIP could truly replace traditional phones.

VoIP is susceptible to worms, viruses and hacking, although this is very rare

and VoIP developers are working on VoIP encryption to counter this.

LESSON 109

INTERNET SERVICES

BLOGGING

A blog (web log or weblog) is one of the popular

activities on the Internet. Most of these blogs are

publicly shared and the authors frequently update

the content on a regular basis.

A blog is usually referred to the text produced by the

author about his or her thoughts, experiences or

interests.

A blog is usually referred to the text produced by the

author about his or her thoughts, experiences or

interests.

The world of blogging is referred as blogosphere.

Another new term is the blogonomics, which refers to

people using the blogosphere to generate money.

The posts to a blog are usually arranged in this order, the most recent

entries will always be on top of the journal.

254

M. Amin, SMK Raja Shahriman

To write a good blog, you need to remember these principles:

use a consistent writing style and appropriate tone for your subject

post often, though your posts are short

allow your readers to eave you comments on your posts

If you would like to search some blogs, you can visit blogarama.com

(www.blogarama.com), which categorises blogs into directories. Following

are several top blogging resources you should check out:

Blogger (www.blogger.com) - owned by Google, one of the free and

easiest to maintain blogging tool.

TypePad (www.typepad.com) - the blog tool that provides more

functionality for a minimal fee.

Movable Type (www.movabletype.org) -  if you have your own

domain site and want to put several blogs together, this is the best

choice

Wordpress (wordpress.org) - an open source blogging tool that

needs a bit of coding to make your blogs more interesting

WORLD WIDE WEB (WWW)

The World Wide Web or the Web consists of a

worldwide collection of electronic documents.

Each electronic document on the Web is called a

web page which can contain text, graphics, audio

and video.

These pages are written in Hypertext  Markup

Language (HTML).

Every website has an address or Uniform

Resource Locator (URL). The URL is formed by the

protocol, domain, directory and the document name.

EMAIL

An electronic mail or email is the transmission of

messages and files via a computer network.

A user utilises an email program to create, send,

receive, forward, store, print and delete email

messages.

Some emails are called web-based email like

Yahoo Mail and Hotmail.

255

THE INTERNET RELAY CHAT (IRC)

The Internet Relay Chat (IRC) is a system for

chatting that involves a set of rules and

conventions, and client/server software.

A chat is a real-time typed conversation that

takes place on a computer. A chat room is a

location on an Internet server that permits users

to chat with each other.

Anyone in the chat room can participate in the

conversation, which usually is specific to a

particular topic.

SEARCH ENGINES

M. Amin, SMK Raja Shahriman

Search engines are special websites on the Internet to help you find

information you need. Different search engines will serve different purposes,

for example:

Google Scholar (http://scholar.google.com/) is for searching

authoritative and scholarly sites.

Google (http://www.google.com/) is for searching valuable or relevant

sites with rankings.

Yahoo News (http://dailynews.yahoo.com) is for searching opinions on

current issues.

Wikipedia (http://www.wikipedia.org/) it is an open source for

encyclopedia

256

LESSON 110

ADVANCED NETWORKING

PERSONAL AREA NETWORK (PAN)

M. Amin, SMK Raja Shahriman

A Personal Area Network (PAN) is a computer network used for

communication among computer devices including PCs, laptops, printers,

telephones, digital cameras, mobile phones, video game consoles and

personal digital assistants, close to one person.

Personal Area Networks may be wired with USB port, Firewire port, Infrared

(IrDA) and Bluetooth technologies. Bluetooth is the popular wireless PAN

used by most people, especially the mobile phone technologies, and it

applies the IEEE 802.15.1 standards.

VIRTUAL PRIVATE NETWORK (VPN)

A Virtual Private Network (VPN) is a network that uses a public

telecommunication infrastructure, such as the Internet, to remote offices or

individuals with secure access to their organisation's private network.

VPN uses tunnelling mechanism to maintain privacy and security of the

data. Tunnelling means transmitting data packets across a public network.

VPN is often used by companies to provide access from their internal

network resources to their home or mobile workers.

257

WIRELESS LAN (WLAN)

M. Amin, SMK Raja Shahriman

Wireless Local Area Network (WLAN) is a type of LAN that uses high-

frequency  radio waves to communicate between nodes. WLAN improves

user mobility, speed and scalability to move around within a  broad coverage

area and still be connected to the network.

The IEEE standard for Wireless LANs is 802.11

WORLDWIDE INTEROPERABILITY FOR MICROWAVE

ACCESS (WiMAX)

Worldwide Interoperability for Microwave Access (WiMAX) is the industry

term for  broadband wireless access network that is developed based on the

IEEE 802.16  standard.

WiMAX is a Wireless Metropolitan Area Network (MAN) technology that will

connect WiFi hotspots to the Internet and provides a wireless extension to

cable and DSL for larger broadband access.WiMAX would operate similar to

WiFi but at higher speeds, over greater

distances and for a greater number of users.

A WiMAX system will have two major parts:

a WiMAX base station, similar in concept to a mobile phone tower

a WiMAX receiver installed at home

258